## Slide 1: FORCE MODELING FOR OBLIQUE CUTTING ON NON-PLANAR SURFACES
Dual degree project
22-6-2017
Department of Mechanical Engineering
Submitted By: Ayush Bandil Guide: Prof. Anirban Guha & Prof. Asim Tewari

## Slide 2: INTRODUCTION
Extremely tight tolerance limit is required in Industries like aerospace and automotive
Limitations of conventional 3-axis milling processes:
  Tolerance limit: High forces result in tool bending
  Tool wear: Quality
  Tool accessibility: free form surfaces

## Slide 3: INTRODUCTION
Two major groups:
  1) Y. Altintas:
      Orthogonal Cutting Data for Ti6Al4V (1995): Experimental
      3-Axis Milling for Ball-End Milling tool (1998)
      3-Axis Milling for Multiple tool (2001)
      5 Axis-Feed Optimization (2008), trajectory shaping (2014), Chattering effect (2016)
  2) Ehran Budak: (Sabanci University)
      Modelling of 5-Axis Milling forces (2005)
      Inconel 718 alloy machining performance for 5-Axis Milling (2013)

## Slide 4: PROJECT OBJECTIVE AND MOTIVATION
Overall aim: General methodology to predict the cutting forces during the 5-axis milling process for:
Any tool geometry
Any feed direction
Any workpiece geometry (edges, corners, step etc.)
Allows surface roughness determination (for machining time optimization)
(Most models exist for ball-end milling tool, horizontal feed and planar surfaces)

## Slide 5
Feed
Normal
Cross feed
lead
tilt
- Lead and tilt

## Slide 6
Feed
z
Cross feed
Normal
x
y
radial
tangential
axial
- Different coordinate systems

## Slide 7: GEOMETRICAL MODELLING OF BALL-END MILL
Step 1
Mathematical formulation of the Tool Envelope
Discretization of Surface Points
Step 3
Identification of the Engagement Region
Step 4
Defining chip dimensions
Step 5
Computation of forces and torque
Step 2

## Slide 8: Different Types of Models Developed
Model 1: Ball-End Mill Cutting Planar Surface having only Horizontal Feed
Model 2: Ball-End Mill Cutting Planar Surface
Model 3: General Milling Tool Cutting Planar Surface
Extensions
Non-planar surfaces
Surface Roughness

## Slide 9: Flow of WinForms
Tool Selection Form
Tool Parameters Form
Select Surface Form
Tool Initial Position and Machining Parameters
Task Selection Form
-Generate Tool Profile
-Generate Custom Surface
-Get Forces and Torque
-Get Lead and Tilt
-Get Engagement Region
-Step Over
- Code written in C# using IDE Microsoft Visual Basic Studio
- 6000+ lines

## Slide 11: Model 1: Ball-End Mill Cutting Planar Surface having only Horizontal Feed

## Slide 12
Ref: http://www.sgstool.com/images-dev/_products/series-1b.jpg

## Slide 13: STEP 1: TOOL ENVELOPE FORMULATION
  Flutes or cutting edge: helix angle i0
  Cutting edge parameters:
  Distance from tool tip along tool-axis (Z)
  Local radius r(z)
  Axial immersion angle
  Lag angle Ψ: angle on x-y plane in TCS between the line which connects the cutting point to the tool tip
  Radial Immersion angle
Helical cutting edges on ball end mill envelope

## Slide 14
  In Tool Coordinate System:
  𝑥𝑥𝑡𝑐𝑠(𝑧) = 𝑟(𝑧) ∗ sin𝛷(𝑧)
  𝑦𝑦𝑡𝑐𝑠(𝑧) = 𝑟(𝑧) ∗ cos𝛷(z)
  𝑧𝑧𝑡𝑐𝑠(𝑧) = 𝑧
Angular incremental (𝑑𝜃) and axial incremental (𝑑𝑧) values: to control the density
  Number of angular integration points (𝐾𝑝)
  𝐾𝑝 =
  Axial integration points (𝐿𝑝)
  𝐿𝑝 =
Discretized points in FCN coordinate system envelope
STEP 2: DISCRETIZATION OF SURFACE POINTS

## Slide 15: STEP 3: IDENTIFICATION OF CUTTING ZONE
  Identified by removing two sets of points from the set of cutting points:
  Points above the cutting depth
  Points lying opposite to the direction of the feed in FCN coordinate system
  Logical Matrix (LG)
Discretized points in FCN coordinate system envelope
Top view of discretized points below the cutting depth
for -200 lead 300 tilt
Top view of discretized points in the cutting zone
for -200 lead 300 tilt

## Slide 16: STEP 4: CHIP DIMENSIONS
The forces generated depend on the geometry on the chips formed.
There are three geometric parameters which are as follows:
  Chip thickness:
  Chip width: projected length of an element in the direction of cutting velocity:
  Chip length: distance between two adjacent cutting points:

## Slide 17: STEP 5: COMPUTATION OF FORCES
Forces in FCN coordinate system
edge forces + cutting forces
radial
tangential
axial
X
Y
Z
X
C
F
N

## Slide 18: Model 2: Ball-End Mill Cutting Planar Surface

## Slide 19: Model 2: Ball-End Mill Cutting Planar Surface
Previous model is no longer valid:
Depth is continuously changing due to vertical feed
Engagement region is dynamic (updated at every angular movement)
Chip thickness value is no longer valid
Changes from previous model:
Engagement region determination methodology
Global Coordinate System
Chip dimensions calculation

## Slide 20
Z
Engagement region determination methodology
Step 1: Geometry Check
GCS: Global Coordinate System
i,j point discretization identifier
If , then the point does not lie in the cutting region (engagement region).

## Slide 21
Engagement region determination methodology
Step 2: Surface normal vector check
If then point does not lie in the cutting region or engagement region.

## Slide 22
Chip Thickness calculation
tn
C
St
-Z
X

## Slide 23: Model 3: General Milling Tool Cutting Planar Surface
Previous model is no longer valid:
Tool surface envelope
Engagement region determination methodology (tool center is not defined)
Chip thickness calculation methodology
Extensions
Non-planar surfaces
Surface Roughness

## Slide 24
Tool Surface Envelope declaration
R
Rr
Rz
α
β
h
D
Z
u
-Seven independent parameters:
D, R, Rr, Rz, ,
- Constraints in these parameters
e.g.
- Discretization parameters:

## Slide 25
Discretization of Surface
Nine Commonly used tools:
Cylindrical-end Mill
Ball-end Mill
Bull Nose-end mill
Taper-end mill
Taper ball-end mill
Cone-end mill
Rounded-end mill
Inverted cone-end mill

## Slide 26
Engagement region determination methodology
Step 1: Geometry Check
GCS: Global Coordinate System
Z
If then point does not lie in the cutting region

## Slide 27
Chip Thickness calculation
Z
Chip thickness is the component of
along the surface normal vector at the point.

## Slide 28
Engagement Zone for Non-Planer Surfaces
Z

## Slide 29
Engagement Zone for Non-Planer Surfaces
Case: Step Surface
The point does not lie in the engagement region in the following conditions:
If and
If and

## Slide 30
Step Over and Surface Roughness
Previous cut
Present cut
Z
Y
t
First Cut, following cut, step over, scallop height

## Slide 31
RESULTS AND VALIDATION

## Slide 32: CASE: Inputs parameters: Diameter, D = 19.05mm Helix angle, i0 = 300 Rake angle, = 00 Number of flukes, Nf = 1 Spindle speed, n=269 rpm Table feed, St = 13.6652 mm/min Depth of cut = 6.35mm Lead angle = 00 Tilt angle = 00
1 cutting edge
Variation of F, C and N forces with rotational angle
As the cutting edge starts coming out of the cutting region all the three components start tending to zero.
Ref: P. Lee and Y. Altintas, “Prediction of ball end milling forces of orthogonal cutting data”

## Slide 33: CASE: Inputs parameters: Diameter, D = 19.05mm Helix angle, i0 = 300 Rake angle, = 00 Number of flukes, Nf = 1 Spindle speed, n=269 rpm Table feed, St = 13.6652 mm/min Depth of cut = 6.35mm Lead angle = 00 Tilt angle = 00
In this case, the ball-end tool has only 1 cutting edge.
Variation of F C and N forces with rotational angle
As the cutting edge starts coming out of the cutting region all the three components start tending to zero.

## Slide 34: Determining Lead and Tilt Angles
Depth of cut = 2.5mm
Lead and tilt angles for minimum force on
the cutting tool are 200 and 40 respectively.
Depth of cut = 5mm
Lead and tilt angles for minimum force on
the cutting tool are 340 and 80 respectively.
As we increase the depth of cut, the lead and tilt angles also need to be increased (magnitude) to get the minimum value of Fxy_max

## Slide 35
CONCLUSIONS AND FUTURE SCOPE

## Slide 36
On hitting an step, the rate of change of forces in the starting zone is much more compared to later zone

## Slide 37
Keeping all the machining parameters constant, inverted cone end mill experiences the maximum amount of resultant force and torque and cone end mill experiences the minimum amount of resultant force and torque

## Slide 38
Forces and torque required in the case when tool has horizontal as well as vertical feed of is much larger when the case when tool has only horizontal feed
-Z
X

## Slide 39
As the number of flutes increase, the force and torque experienced by the tool are more evenly distributed
Number of flutes = 2
Number of flutes = 3

## Slide 40: SHORTCOMINGS OF THE CURRENT MODEL
Orthogonal Cutting Data is based on empirical results obtained after conducting experiments and then fitting a regression model, Hence the results obtained from OCD are not necessarily accurate.
The model has been developed for only Titanium alloy.
The model considers the tool is always ideal, rigid, edges are always sharp and do not wear while machining, whereas in real life tool wears out due the cyclic force experienced.
Chips are considered to be in most ideal form also known as undeformed chips. In reality, chips dimensions are different and chips interfere in cutting process.

## Slide 41: FUTURE SCOPE
The current model can be extended to automate the selection of tilt angle and step over to optimize the machining time and surface roughness.
Using this model, the energy lost in cutting () and energy dissipated as heat can be known, the model can be extended to incorporate lubrication and cooling aspects.
Automation can be done in terms of path selection of the tool given the initial and final workpiece model cutting within the surface tolerance limit.
CAM/CAD models can be integrated with the current model. Workpiece surface can be dynamically updated and the combination of the lead and tilt angles can be obtained at each point of time to optimize the entire process in terms of machining time.
This model can become the input for vibration and chatter modeling of the machining processes

## Slide 42
THANK YOU